## Slide 1
Q&A PPT

## Slide 2
Slide 2 – Engineering Concepts: Control & Auto
Answer: Raw sensor values are not always accurate. Calibration compares sensor readings with known reference values to determine the correct conversion equation. This reduces measurement error and increases the accuracy of the entire system.

## Slide 3
Answer: The main contribution is integrating five sensing modalities into one intelligent embedded system that performs automatic decision-making, controls actuators, records timestamped data, and provides reliable security and fire protection while remaining modular, scalable, and easy to maintain.
Q1. What is the biggest engineering contribution of your project?
01

## Slide 4
Q2. Why did you use two sensors for entry detection instead of only one?
Answer: We used sensor fusion to improve reliability. The TCRT5000 detects the presence of a person, while the load cell confirms that someone is physically standing on the platform. The door requests the PIN only when both conditions are true. This greatly reduces false alarms caused by reflections, shadows, or nearby objects.
02

## Slide 5
Q3. Why is calibration important?
Answer: Raw sensor values are not always accurate. Calibration compares sensor readings with known reference values to determine the correct conversion equation. This reduces measurement error and increases the accuracy of the entire system.
3

## Slide 6
Q4. What are the main safety features of your system?
Answer: The system operates on low-voltage DC, uses relays to isolate high-current loads from the Arduino, protects inductive loads, separates water from electronics, and keeps the controller isolated from the actuator power supply.
4

## Slide 7
Q5. For future, what improvements would you add?
Answer: We would replace the DHT11 with a more accurate sensor, add smoke and gas sensors, include Wi-Fi notifications, use an SD card and RTC for permanent logging, improve the load-cell calibration, and design a professional PCB.
5

## Slide 8
Q6. How did you verify that your sampling rate was appropriate?
Answer: Fast-changing signals such as infrared detection are read continuously, while slower environmental sensors like DHT11 are sampled every five seconds. This provides sufficient accuracy while reducing unnecessary processing.
6

## Slide 9
Q7. Why did you use relays?
Answer: Relays electrically isolate the Arduino from high-current loads such as the pump, fan, and humidifier, protecting the controller.
7

## Slide 10
Q8. Which parts of your project make it reliable?
Answer: Reliability is improved through dual-sensor entry confirmation, non-blocking software, finite-state-machine control, hysteresis for fan operation, relay isolation, timestamped logging, and automatic fault detection.
8

## Slide 11
Q9. How do you guarantee that one subsystem does not interfere with the other?
Answer: The security and fire subsystems use independent variables, independent decision logic, and separate state machines. They share the Arduino hardware but not the decision-making process.
9

## Slide 12
Q10. Which engineering concepts from the Sensors course are implemented in your project?
Answer:
The project also implements threshold-based control, where predefined limits trigger automatic actions such as alarms, pump operation, and fan control. Sensor fusion combines the infrared sensor and load cell to improve entry reliability and reduce false detections. A finite-state machine organizes the fire-response sequence, while EEPROM stores calibration constants so they are retained after power loss. Finally, timestamped CSV data logging supports performance analysis, and automatic actuation controls the servo motor, pump, humidifier, fan, buzzer, and warning LED based on sensor readings.
10

## Slide 13
Q11. Why is timestamped data logging important in engineering systems?
Answer: Timestamped logging provides traceability, allows post-processing and fault analysis, verifies system performance, and makes it possible to import the data directly into Excel or MATLAB for further analysis
11