## Slide 1
SENSORS PROJECT • UPDATED CONTROL LOGIC
Smart Laboratory Security
& Fire Protection
Dual-sensor entry • automatic fire response • timestamped evidence
TEAM
Ali • Makram • Nassim • Mustapha
ARDUINO
CONTROL
IR + kg
ENTRY SECURITY
°C + L/min
FIRE RESPONSE
ALI 1/3

## Slide 2
One controller supports two independent decision paths
ALI 2/3
SMART LABORATORY SYSTEM • 02
ENTRY SECURITY
Infrared detection + entry weight
↓
PIN request → door or sticky alarm
Both sensors must agree before authentication begins.
FIRE PROTECTION
Temperature + humidity + water flow
↓
Pump → flow check → humidifier/fan
Fire decisions never read the load cell.
CORRECTION • The load cell belongs to the entry platform—not a tank and not the fire system.

## Slide 3
Sampling matches how quickly each signal changes
ALI 3/3
SMART LABORATORY SYSTEM • 03
SIGNAL
SAMPLING
WHY
TCRT5000
Every loop
Immediate optical presence
HX711 load cell
When data is ready
Entry-weight confirmation
Keypad
Continuously
15 s inactivity timeout
Flow sensor
Interrupt pulses
Flow calculated every 5 s
DHT11
Every 5 s
Temperature / humidity
Fire state + CSV
Every 5 s
Timestamped status record
The DHT11 changes slowly; a 5-second control/logging interval is stable, readable, and sufficient for the fire sequence.

## Slide 4
Entry is confirmed only when both sensors agree
MAKRAM 1/3
SMART LABORATORY SYSTEM • 04
TCRT5000
infrared = TRUE
HX711 load cell
weight ≥ threshold
AND
personDetected
= TRUE
THEN
REQUEST
PIN
Truth table
IR
WEIGHT
RESULT
0
0
No trigger
1
0
No trigger
0
1
No trigger
1
1
Request PIN
Sensor fusion rejects an infrared reflection without weight and a weight change without infrared presence.

## Slide 5
Confirmed presence triggers the full security response
MAKRAM 2/3
SMART LABORATORY SYSTEM • 05
1
CONFIRM
IR AND weight
2
REQUEST PIN
Voice prompt
3
VALIDATE
15 s • 8 digits
4A
CORRECT
Door opens 5 s
4B
3 WRONG
Sticky alarm
Automatic response: the servo opens only after a correct PIN; the thief buzzer remains active until a correct PIN clears it.

## Slide 6
The fire controller advances through testable states
MAKRAM 3/3
SMART LABORATORY SYSTEM • 06
IDLE
FIRE
DETECTED
PUMPING
HUMIDIFYING
STABLE
BLOCKED
latched
> 27°C
pump ON
55 s + flow
≥ 70% RH
≤ 0.05 L/min
next cycle → IDLE
The pump runs for the full 55 seconds unless flow indicates blockage. Temperature falling does not stop the pump early.

## Slide 7
Timestamped CSV makes system behavior visible
NASSIM 1/3
SMART LABORATORY SYSTEM • 07
SERIAL MONITOR • 9600 baud
timestamp,temp,humidity,entry_weight,IR,weight,person,flow,state,wrong
15000,25.4,54.0,68.2,1,1,1,0.00,IDLE,0
20000,28.1,55.2,0.0,0,0,0,0.12,PUMPING,0
Each row is machine-readable and immediately importable into Excel, MATLAB, or Python.
What the evidence proves
Real-time system status
Sensor fusion is visible
Fire states are traceable
At least 60 s can be logged
CSV every 5 seconds

## Slide 8
Calibration turns raw readings into measurements
NASSIM 2/3
SMART LABORATORY SYSTEM • 08
kg
1 REFERENCE
Use at least three known weights or flow volumes.
CSV
2 RECORD
Save raw and reference values in the calibration CSV.
±%
3 VALIDATE
Calculate factor, curve, and before/after error.
EEPROM
4 PERSIST
Store validated load-cell and flow factors in EEPROM.
TCRT5000 threshold is tuned for distance and lighting. If EEPROM is blank, dedicated constants provide safe defaults.

## Slide 9
Protected power separates sensors from actuators
NASSIM 3/3
SMART LABORATORY SYSTEM • 09
5 V LOGIC & SENSORS
Arduino Uno
TCRT5000 + HX711 load cell
DHT11 + flow-sensor signal
Keypad, DFPlayer, status LED
RELAYS
→
≤ 12 V DC ACTUATORS
Pump • humidifier • fan • servo
No direct mains connection
Fuse / diode / relay protection
Regulated supplies and common ground
Pin-to-pin wiring documented in Fritzing
In the final Fritzing schematic, the load cell is grouped with entry sensing—not with fire protection.

## Slide 10
Fail-safe states and modular code improve reliability
MUSTAPHA 1/3
SMART LABORATORY SYSTEM • 10
FAIL-SAFE
DHT failure skips the cycle; relays initialize OFF.
ROBUST
BLOCKED is latched; flow is checked while pumping.
MAINTAINABLE
Separate .ino modules, named thresholds, EEPROM calibration.
POWER-AWARE
Pump, humidifier, fan, servo and buzzer run only when needed.
Non-blocking timers keep monitoring active while alarms and actuators are operating.

## Slide 11
Low-cost modules keep the prototype affordable
MUSTAPHA 2/3
SMART LABORATORY SYSTEM • 11
COST CONSIDERATIONS
Arduino-class controller and common sensors
Replaceable modular components
Protection and calibration receive priority
No expensive cloud service is required
Trade-off: DHT11 and hobby modules reduce cost, but industrial deployment needs higher-grade sensors.
SCALABILITY ROADMAP
NOW
Dual entry + fire response
NEXT
Smoke / gas sensing + SD log
LATER
RTC, remote alerts, redundancy
DEPLOY
Industrial sensors and enclosure

## Slide 12
Lecture concepts become a measurable safety workflow
MUSTAPHA 3/3
SMART LABORATORY SYSTEM • 12
Signal conditioning
Calibration, thresholds, error
Sensor fusion
IR AND weight confirmation
Embedded timing
Interrupts + non-blocking timers
Control logic
State machine + automatic response
Data acquisition
Timestamped CSV + analysis
WHAT THE VIDEO DEMONSTRATES
60 s
continuous simulation
and timestamped logging
Dual-sensor entry → PIN response
Fire threshold → pump / flow / humidity
Serial Monitor → real-time CSV status
Two sensors confirm entry. Independent fire logic acts automatically. Every step is observable.